## Slide 1: Kashmir Valley Transit Rationalisation Engine v3.3
Technical Architecture, Methodology & Results

## Slide 2: Project Scope & Objectives
Data-driven route optimisation for Srinagar / Kashmir Valley.
- 342 active in-scope routes within bounding box (33.5°-34.5° N, 74.4°-75.2° E)
- SSCL Backbone: 30 hardcoded e-bus routes (15-min headways)
- Addresses over-served corridors and transit deserts
- Engine provides automated frequency planning and fleet allocation

## Slide 3: Engine Outputs (v3.2/3.3)
Generated Assets:
- Route Frequency Plan (XLSX): 342 routes, fleet counts, headways
- Master Transit Map (HTML): Interactive Folium map with POI/Trunk layers
- Passenger Impact (CSV) & Rationalisation Log (CSV)
- GeoJSON network map for GIS integration

## Slide 4: Key Directions & Network Stats
Network Efficiency (12-month data calibration):
- Deduplicated Population Served: 1,158,399 (69.8% of CMP 2024 total)
- Active Fleet Required: 1,307 buses (Total in-scope: ~1,059)
- Priority Bands: 134 High Priority (HP), 100 Medium Priority (MP), 3 Low (LP)
- Merged/Absorbed: 105 redundant routes merged into Trunks

## Slide 5: Methodology: Data Ingestion & Spatial Analysis
Pipeline Phase 1 & 2:
- OSRM Routing: Bounding box truncation & geometry extraction
- Population Scoring: 400m walk catchments via WorldPop raster
- POI Gravity (3-Tier): Year-round, Secondary, Seasonal (Tourist)
- Seasonal Toggle: Winter mode zeroes Tier-3 tourist POIs

## Slide 6: Methodology: Route Classification & Fleet
Pipeline Phase 3 & 4:
- Union-Find clustering for overlapping corridors (threshold=65%)
- CDI (Composite Demand Index): Pop(0.5) + POI(0.5)
- Fleet Allocation: ceil(Cycle_Time / Headway)
- Congestion factors: 2.2x Downtown, 1.4x Peri-urban, 8-min Jhelum bridge penalty

## Slide 7: v4 Horizons (Future Work)
Planned Upgrades:
- Network-graph walksheds (accounting for Jhelum/Lake barriers)
- Tourist surge volume modelling
- Demand elasticity (Mohring effect)
- Per-route AFC validation