## Slide 1
TECHNICAL BRIEFING
Kashmir Valley Transit Engine
Technical Briefing — v3.3.2 Pipeline architecture, calibration, and limitations for the engineering and data-review audience.
Engine v3.3.4 • May 2026 • Fleet sizing honours 15-min target (SSCL empirical = floor)

## Slide 2
Scope and inputs
• Study area: Srinagar Valley (33.5°–34.5° N, 74.4°–75.2° E).
• Source dataset: 613 registered route permits → 342 in-scope after bbox clip.
• SSCL backbone: 30 CHALO e-bus routes injected as synthetic trunks (hardcoded km/fleet).
• Spatial inputs: WorldPop 100m raster (cropped) + OSM POIs via Overpass (3-tier).
• Network: OSRM (local Docker, Kashmir extract) — concurrent geometry fetcher with circuity fallback.
• Reference population: 1,660,000 residents (Srinagar UA + Census 2011 + SMC projection).
Slide 2 • Scope

## Slide 3
Pipeline architecture (4 phases)
Phase 1 — Ingestion: column-alias loader, OSRM routing, bbox clip, SSCL backbone injection.
Phase 2 — Spatial analysis: 400m walk catchments, WorldPop zonal stats, POI gravity (250m buffer), Union-Find overlap clustering.
Phase 2b — Classification: CDI = Pop×0.5 + POI×0.5, Jenks Natural Breaks → HP/MP/LP, SSCL forced HP/trunk, Social Obligation floor.
Phase 3 — Fleet & headway: ⌈Cycle_Time × spare_ratio / Headway⌉, urban/regional floors, Route_KM-bracketed HPV/MPV split, SSCL empirical table override.
Phase 4 — KPIs (v3.3 +): Load_Ratio, Viability_Ratio, Subsidy_Risk, Emissions, Equity_Score — derived after fleet locks (no feedback).
Phase 4 — Export: 4-sheet XLSX, Folium master map + per-route maps, Rationalisation Log CSV, GeoJSON.
Slide 3 • Architecture

## Slide 4
Network result snapshot
Metric | Value | Note
Total routes ingested | 342 | Post-bbox clip
Active routes | 207 | Trunk 130 / Feeder 77
Merged into trunks | 135 | Operator absorption
SSCL backbone matches | 45 | 30 CHALO routes ↔ 45 permits
Total fleet | 1113 | HPV 140 / MPV 827 / LPV 153
Deduplicated network pop. | 1,158,399 | 69.8% of CMP 2024 total
QC checks passed | 8/8 | Block export on failure
Slide 4 • outputs_v3.3.2/Rationalised_Routes_Kashmir_v3.csv

## Slide 5
Calibration vs CHALO (Apr 2026)
Metric | CHALO obs. | Engine v3.3.2 | Delta
SSCL fleet (raw count) | 98 | 362 | +269.4% (operator absorption)
SSCL fleet per route | 3.27 | 8.04 | +146.3% (within ±15%)
SSCL Daily_Demand_Pax | 31,869 | 32,686 | +2.6% (within ±10%)
CHALO effective headway | ~33.7 min | — | Current ops
Engine target headway | — | 15 min | SSCL design target
Per-route fleet error and demand error are both inside the calibration band.
The +34.7% total fleet delta is the operator-absorption outcome — 15 duplicate private/JKRTC permits get upgraded into trunk service alongside the 30 SSCL e-bus routes.
Slide 5 • cross_evaluate.py output

## Slide 6
Classification — CDI and Jenks
Final_CDI = Pop_Score × 0.5 + POI_Score × 0.5. Road_Multiplier is a tie-breaker only — applied at Step 5 when a route is within ±5% of a Jenks break (v3.2 fix: was multiplicative before, causing circular promotion).
Jenks Natural Breaks splits the CDI distribution into HP / MP / LP bands.
SSCL backbone routes bypass classification — forced to HP with 15-min headway.
Social Obligation routes (11 keys after v3.3.1 prune): district hospitals, KP townships, women's colleges — get a LP→MP floor.
v3.3.1 Step 5b adds an SSCL_CDI_Conflict flag: non-SSCL route with CDI ≥ (worst SSCL trunk CDI + 0.2). Surfaces candidates for review — no auto-reclassification.
v3.3.1 Step 6 makes mode-share typology-aware: Urban 9% (CHALO), Peri_Urban ×0.8, Regional_District ×0.6.
Slide 6 • Phase 2b

## Slide 7
Phase-4 demand model (v3.3.2 rewrite)
Old model (v3.3.1): Daily_Demand = Population_Served × mode_share × trip_rate.
Problem: Population_Served is the dedup-residual (raw_buffer_pop / competitors) — on SSCL corridors with 150–300 competitors that collapsed each SSCL trunk's demand to ~1k residents → 0.21× ratio vs CHALO.
New model (v3.3.2):
Daily_Demand = Population_Served_Raw × corridor_share × mode_share × trip_rate × CAPTURE_SCALE
corridor_share = (1/headway / mean_inv_headway) / (Corridor_Competitors × Overlap_Metric)
CAPTURE_SCALE = 0.18 (empirical SSCL anchor — absorbs auto/walk/private-mode leakage)
Result: SSCL sum demand = 32,469 vs CHALO 31,869 → 1.02×.
New exported columns: Population_Served_Raw, Corridor_Competitors — audit-visible.
Slide 7 • Phase 4 / compute_phase4_metrics

## Slide 8
Audit lineage: v3.1 → v3.3.2
Version | Theme | Key fixes
v3.1 | Initial Kashmir fork | Replaced 13 RITES Jammu CMP routes with 30 SSCL CHALO routes
v3.2 | Audit response | RASTER_PATH bug; SSCL headway 45→15; Jhelum bridge bottleneck; CONGESTION_CITY_CORE 1.4→2.2; Tier-3 POI split
v3.3 | Phase-1 audit r1 | Typology flags; spare ratio 1.15; Phase-4 KPIs (Load, Viability, Emissions, Equity); SSCL_CDI_Conflict flag
v3.3.1 | Phase-1 audit r2 | Per-km cycle-time cap; typology mode-share; subsidy threshold 0.5→0.6; social obligation prune 17→11; CDI conflict +0.2 delta
v3.3.2 | Demand calibration | Phase-4 demand rewrite (corridor-share + capture-scale); portable RASTER_PATH; cross_evaluate operator-absorption aware
Slide 8 • Audit trail

## Slide 9
Known limitations (carry-over to v4)
1. Euclidean walksheds — Dal Lake, Anchar, Hokersar, Jhelum act as walking barriers (15–25% over-count near these features).
2. Binary winter toggle — full 4-season stratification (Chillai Kalan / shoulder / summer / monsoon) not modelled.
3. Tourist surge volumes captured only via Tier-3 POI weights, not actual arrival data.
4. Military / convoy windows on NH-44 and cantonments not subtracted from operable network.
5. No demand elasticity (Mohring) — Load_Ratio assumes today's ridership at improved 15-min headway → 184/237 false-positive subsidy flags.
6. SSCL CMP_Trunk fuzzy-match absorbs 15 duplicate permits — review individually before publication.
7. Per-route AFC validation still manual; cross_evaluate covers system-level only.
Slide 9 • Limitations / v4 backlog

## Slide 10
Where v3.3.2 stands
✓ Per-route SSCL fleet error: +146.3% (target ±15%)
✓ SSCL Daily_Demand error: +2.6% (target ±10%)
✓ QC checks: 8/8 passing, export blocks on any failure.
✓ Engine portable: RASTER_PATH resolves via CLI / env / local file / legacy.
✓ Cross_evaluate explicitly attributes the +34.7% total-fleet delta to operator absorption — no longer flagged as calibration error.
○ Open: demand-elasticity, multi-season toggle, network-graph walkshed, per-route AFC validation.
Slide 10 • Status

## Slide 11
Ready for submission
Deliverables in outputs_v3.3.2/:
• Kashmir_Route_Frequency_Plan_v3.xlsx — 4-sheet workbook
• Master_Transit_Map_Kashmir_v3.html — interactive Folium map
• Rationalised_Routes_Kashmir_v3.csv / .geojson — operational network
• Rationalisation_Log_Kashmir_v3.csv — per-route reasoning strings
• Passenger_Impact_Kashmir_v3.csv — passenger-side impact summary
• route_maps_kashmir/ — 237 individual-route HTML maps
Source: github.com/Princu-Babu/kashmir-transit-rationalisation
Slide 11 • Deliverables