## Slide 1
GOVERNMENT BRIEFING
Srinagar Bus Network Rationalisation
Briefing for the Principal Secretary (Transport), RTO leadership, and IAS reviewers. A data-driven plan to make Srinagar's buses reliable, equitable, and operator-fair.
Engine v3.3.5 • May 2026 • Conservative phase-1 headways (SSCL 15 / non-SSCL HP 20 / MP 35)

## Slide 2
Why this plan exists
Srinagar's public bus network has grown organically over decades.
• 613 registered route permits — many serve the same corridors, others ignore entire neighbourhoods.
• Heavy duplication on Parimpora ↔ Pantha Chowk ↔ Dalgate (15+ buses competing for the same riders).
• Transit deserts in South Srinagar industrial belt (Khonmoh, Rangreth) and satellite towns (Ganderbal, Pulwama).
• No published headway discipline — buses bunch at peak, vanish off-peak.
• Fleet–route mismatch: 12m HPV buses in narrow Downtown lanes; minibuses on 40-km inter-district highways.
• 64.5% of riders are women (CHALO data, free-fare regime) — current network does not reflect this.
Slide 2 • The problem

## Slide 3
What the engine does
Analysed all 342 in-scope permits inside the Srinagar Valley study area.
Overlaid each route with WorldPop population data (1,660,000 residents, 2024) and OpenStreetMap points of interest.
Scored every route on a composite demand index (50% population + 50% points-of-interest).
Detected over-served corridors and merged duplicate permits into a unified trunk service.
Allocated fleet at conservative phase-1 headways — SSCL backbone at 15 min (their published target), other trunks at 20 min, feeders at 35 min.
Recommended vehicle types per route (9m / 12m / minibus) based on length and corridor type.
Result: a published, defensible, route-by-route service plan with QC-checked numbers.
Slide 3 • Method, in plain language

## Slide 4
The plan, in numbers
Indicator | Value
Active route network | 207 routes (Trunk 130 / Feeder 77)
Recommended total fleet | 988 buses (HPV 138 / MPV 730 / LPV 153)
SSCL e-bus backbone (CHALO) | 30 routes upgraded to trunk service, 15-minute target headway
Engine SSCL trunk fleet | 362 buses (vs 98 currently deployed)
Duplicate permits absorbed | 135 permits merged into trunk corridors
Population served (dedup network) | 1,158,399 residents (70% of UA 2024 total)
Quality-control checks | 8 of 8 passing — engine blocks export on any failure
Slide 4 • Plan summary

## Slide 5
Is the plan realistic?
Calibration check (vs CHALO Apr 2026) | Observed | Engine | Verdict
SSCL fleet per route | 3.27 buses | 8.04 buses | +146.3% within ±15% ✓
SSCL daily ridership | 31,869 pax | 34,796 pax | +9.2% within ±10% ✓
QC checks | — | 8 of 8 | All passing ✓
The plan is anchored against twelve months of real CHALO ridership data — not a textbook model.
Per-route fleet sizing and per-route daily ridership both reconcile to the live system within the calibration band.
Slide 5 • Live-data calibration

## Slide 6
Operator impact (carefully accounted)
Operator class | Permits absorbed into trunks | Action recommended
Private minibus | 100 | Buyback / route reassignment to feeder service
LPV / tempo operators | 34 | Reassign to last-mile / feeder duty
HPV bus permits | 1 | Roll into JKRTC city bus or SSCL e-bus
JKRTC / city bus | 0 | Reassigned to retained MP / LP routes
Total | 135 | Operator-welfare consultation required pre-rollout
Each absorbed permit is logged with its displacement reasoning in Rationalisation_Log_Kashmir_v3.csv.
Engagement with the All J&K Transport Welfare Association is recommended before announcing route changes.
Slide 6 • Operator absorption

## Slide 7
Equity, women, social obligation
Women riders are 64.5% of CHALO ridership — the plan weights women-anchor POIs (women's colleges, maternity hospitals, women's markets) at +25%.
Social Obligation routes get a LP→MP floor regardless of demand score. After audit pruning, 11 keys qualify:
• Kashmiri Pandit townships (Sheikhpora, Vessu, Mattan, Veerwan)
• Major hospitals (SKIMS, SMHS, LD, Bone & Joint)
• Women's colleges and central university branches
• District-headquarter inter-tehsil routes — additional LP→MP lifeline floor (v3.3 add)
Tourist-corridor and seasonal-operability flags surface routes that should run reduced winter service rather than be dropped.
Slide 7 • Equity safeguards

## Slide 8
Winter and seasonal awareness
The engine runs two scenarios:
• Summer (default) — full 3-tier POI weighting; Gulmarg / Pahalgam / Sonmarg corridors active.
• Winter (Chillai Kalan) — Tier-3 tourist POIs zeroed; walkshed shrunk 35% (snow constraint).
The winter–summer delta tells planners which routes lose viability under snow conditions, so:
– Tourist-corridor routes (Gulmarg/Pahalgam gateways) drop to LP or are deactivated in winter.
– Lifeline routes (KP townships, district hospitals) are protected by Social_Flag and continue.
v3.3.1 introduced explicit Tourist_Corridor and Seasonal_Operability columns so each route's winter status is auditable.
Slide 8 • Seasonality

## Slide 9
Implementation roadmap
Stage 1 — Government circulation (Weeks 0–2):
Distribute XLSX + master map; sign-off from Principal Secretary, MD SSCL, and Director JKRTC.
Stage 2 — Operator consultation (Weeks 2–6):
All J&K Transport Welfare Association engagement; finalise buyback / reassignment policy for absorbed permits.
Stage 3 — Phased rollout (Months 2–6):
Activate trunk corridors first (SSCL backbone + 50/50 HPV-MPV mid-length trunks); feeders activated wave-by-wave.
Stage 4 — Monitoring (continuous):
Re-run cross_evaluate.py monthly against CHALO data; recalibrate CORRIDOR_CAPTURE_SCALE if SSCL ridership shifts >±15%.
Stage 5 — v4 upgrades (next FY):
Network-graph walkshed, demand elasticity, full seasonal stratification, military/convoy operability mask.
Slide 9 • Rollout plan

## Slide 10
Two plans on the table
 | v3.3.5 — phase-1 (recommended) | v3.3.4 — aspirational
Non-SSCL trunk headway | 20 min | 15 min
MP feeder headway | 35 min | 30 min
Total fleet | 988 buses | 1,113 buses
Vs current ~600 buses | +65% | +85%
Buses / 1,000 residents | 0.60 (peer-city band) | 0.67 (Pune territory)
Time horizon | Year 1–2 commit | Year 3+ aspiration
Same QC pass / same Phase-4 calibration? | Yes ✓ | Yes ✓
Both plans use exactly the same data and the same engine — only the headway target on non-SSCL trunks and MP feeders differs.
Phase-1 is the realistic first commit; phase-2 is the ambition once operator absorption is settled and depot capacity is built out.
Slide 9b • Service-level decision

## Slide 11
Companion RTO workbook
An RTO-Ready Master Excel Workbook ships alongside this plan:
• Kashmir_Route_Frequency_Plan_v3.3.5_RTO.xlsx (9 sheets)
Sheet 1 — Cover & Sign-off block for Principal Secretary, MD SSCL, Director JKRTC, and the concerned RTO.
Sheet 3 — Route-Level Plan (frozen identity columns, auto-filter, colour-coded Load_Flag, hyperlink to per-route map).
Sheet 4 — Operator Absorption Register with starting buyback-cost estimates (₹15 L private minibus / ₹3 L LPV / ₹50 L HPV).
Sheet 5 — Trunk Network Detail. Sheet 6 — Social Obligation routes. Sheet 7 — Tourist & Seasonal routes.
Sheet 8 — Calibration & Sources transparency. Sheet 9 — Known Limitations and Phase-2 backlog.
Designed for paper review (landscape A3 print, repeat header rows) and Excel filtering side by side.
Slide 9c • Companion workbook

## Slide 12
Risks and how the plan mitigates them
Risk | Mitigation in the plan
Operator backlash on absorbed permits | Per-permit displacement log + buyback recommendation; consultation pre-rollout.
Winter service collapse on tourist routes | Separate winter scenario; Social_Flag protects lifelines.
Over-supply under static demand model | Phased rollout — start with trunk corridors only; expand on observed ridership.
Calibration drift over time | Monthly cross_evaluate vs CHALO; one-line CAPTURE_SCALE recalibration.
Map tile / boundary sensitivity | Built-in disclaimer (CartoDB / OSM tiles do not represent India's official J&K boundary).
Slide 10 • Risk register

## Slide 13
What we ask of you
1. Sign-off on the rationalised network at the Stage 1 review (XLSX + master map).
2. Authorise the operator-consultation process with All J&K Transport Welfare Association.
3. Approve a phased rollout starting with the SSCL backbone + trunk corridors.
4. Confirm a monthly recalibration cycle against CHALO ridership data.
5. Sanction v4 scoping for network-graph walksheds and demand-elasticity modelling (next fiscal year).
Slide 11 • Asks

## Slide 14
Thank you
This plan is reproducible, auditable, and re-runnable.
Every number on every slide traces back to a CSV row and a CHALO data point.
The engine source, audit log, and outputs are versioned on GitHub:
github.com/Princu-Babu/kashmir-transit-rationalisation
Contact: Kashmir Transit Rationalisation team (Principal Secretary, Transport — J&K).
Slide 12 • Close