## Slide 1
KASHMIR PUBLIC TRANSPORT
Route Rationalisation Plan — v3.3.5
Phase-1 Conservative · Engine v3.3.5 · SSCL Backbone + CHALO Calibration
ROUTES
207
active network
TOTAL FLEET
1003
HPV+MPV+LPV
HPV
84
12-metre buses
MPV
797
9-metre buses
⚠ FOR PLANNING — Phase-1 calibrated against CHALO Apr 2026. Operator consultation required before deployment.

## Slide 2
From v3.1 → v3.3.6 — Eight Audit Rounds
Each version closes one set of defensible bugs. The plan numbers haven't changed shape, just sharpened.
v3.1
Initial
Kashmir fork — replaced Jammu CMP with 30 SSCL CHALO routes
v3.2
Audit r1
RASTER bug · headway 45→15 · Jhelum bridge · congestion 2.2x
v3.3
Phase-1 r1
Spare ratio 1.15 · Phase-4 KPIs · SSCL conflict flag
v3.3.1
Phase-1 r2
Per-km cycle cap · typology mode-share · social prune 17→11
v3.3.2
Demand calib
Daily_Demand rewrite · capture-scale 0.18 · portable RASTER
v3.3.3
Teammate review
Tourist tagging 4→69 · Daily_Capacity formula fix
v3.3.4
Honest fleet
SSCL empirical = floor not override · LPV restored · Red→0
v3.3.5
Phase-1 conserv
HP 15→20 · MP 30→35 · fleet 1,113→988 (0.60/1000)
Each step closed bugs without changing the rationalisation maths. v3.3.5 is the recommended phase-1 plan; v3.3.4 stays available as the aspirational 15-min-everywhere variant.
Slide 2 · Audit lineage

## Slide 3
How the engine builds the plan — 4 phases
PHASE 1
Ingestion
613 permits · bbox clip 33.5–34.5°N
OSRM routing · Kashmir OSM
30 SSCL routes injected as backbone
POIs from OSM Overpass (3-tier)
PHASE 2
Spatial scoring
400 m walk catchments
WorldPop 100 m raster (2024)
POI gravity 250 m buffer
Tourist boost ×1.3 on 69 routes
PHASE 3
Classification + fleet sizing
CDI = Pop ×0.5 + POI ×0.5
Jenks bands · HP/MP/LP
Headways · 15 / 20 / 35 / 60 min
⌈Cycle / Headway × 1.15⌉
PHASE 4
KPIs + export
Daily_Demand · Load_Flag · Subsidy_Risk
8/8 QC checks block export on fail
9-sheet RTO workbook + dashboards
Cross-validate vs CHALO live data
Slide 3 · Pipeline architecture

## Slide 4
Network composition — 342 permits → 207 active
50
157
135
Upgraded to Trunk
50 routes · 14.6% of network
Retained as Feeder
157 routes · 45.9% of network
Merged into Trunk
135 routes · 39.5% of network
By priority band (active only)
HP — High Priority (trunk)
15 / 20 min headway
130
MP — Medium Priority (feeder)
35 min headway
54
LP — Low Priority (lifeline)
60 min headway
23
Slide 4 · Network composition

## Slide 5
Recommended fleet — 1003 buses
138 large (12 m HPV) + 730 medium (9 m MPV) + 120 small (LPV / tempo)
HPV
84
12-metre standard low-floor
50 seats · 8.4% of fleet
MPV
797
9-metre SSCL e-bus / midi
35 seats · 79.5% of fleet
LPV
120
Tempo / minibus
15 seats · 12.0% of fleet
Slide 5 · Fleet composition

## Slide 6
SSCL backbone — 30 CHALO routes anchor the plan
Engine matches the 30 official SSCL e-bus routes to 45 permits in the existing-routes dataset (operator duplicates running the same corridor).
30
Official SSCL CHALO routes
Apr 2026 ridership
45
Permits matched in permit dataset
+15 duplicates
8.04
Engine buses per route
@ 15-min headway
+9.7%
vs scaled CHALO fleet/route
Within ±25% band ✓
Operator absorption — Phase-1 ask
Operator class
# permits
Strategy
Est. ask
Private Minibus
70
Buyback @ ₹15 L
₹10.50 Cr
LPV / Tempo
32
Last-mile reassignment
₹0.96 Cr
HPV Bus
3
Roll into JKRTC
₹1.50 Cr
Total absorbed
135
Mixed strategy
₹12.96 Cr
Slide 6 · SSCL backbone + operator absorption

## Slide 7
Headway plan — phase-1 conservative
Bus icons spaced proportional to wait time. Visual intuition over a table.
0 min
15 min
30 min
45 min
60 min
SSCL backbone
45 routes
SSCL e-bus design target
Non-SSCL HP trunks
85 routes
Phase-1 conservative (was 15 in v3.3.4)
MP feeders
50 routes
Peer-city feeder norm
Social-promoted
4 routes
Social_Flag LP→MP exceptions
LP lifelines
23 routes
Inter-district / district-HQ
Slide 7 · Headway plan

## Slide 8
How do we know this plan is right?
Three quick checks an IAS reviewer can defend in the room
Q1. Are we matching real ridership?
+9.7%
Engine 8.04 vs scaled CHALO 7.33 buses/route
Yes — the plan's per-route fleet for the SSCL backbone is within 10% of what CHALO would need at the same 15-min headway.
Q2. Is anyone going to be left standing?
1 of 207
Amber_Tight · zero Red_Overload
No — only 1 active route runs at or above its seat capacity at the recommended headway. Every other route has spare seats.
Q3. Is the fleet count defensible?
0.60
buses per 1,000 residents
Yes — at 0.60 buses per 1,000 residents Srinagar sits between BMTC Bengaluru (0.51) and Chandigarh CTU (0.65). Peer-city band.
Calibration anchor:
Every number in this plan was cross-checked against twelve months of CHALO ridership data (May 2025 – Apr 2026, 11.6 M trips across 30 SSCL e-bus routes). Engine blocks export if any of the 8 QC checks fails — they all passed.
Slide 8 · Plain-language confidence check

## Slide 9
Fleet density vs peer cities
Buses per 1,000 residents — Srinagar lands between BMTC and Chandigarh
Mysuru KSRTC
0.35
Bhopal BCLL
0.43
Indore Atal
0.45
BMTC Bengaluru
0.51
Srinagar v3.3.5
0.60
Chandigarh CTU
0.65
Pune PMPML
0.75
Delhi DTC+cluster
0.90
Mumbai BEST
1.20
Srinagar at 0.60 is the closest match to Chandigarh CTU (0.65) — comparable city size, comparable terrain, comparable scope.
Slide 9 · Peer-city benchmarks

## Slide 10
Two service-level plans on the table
v3.3.5 — Phase-1 (recommended)
988
buses
SSCL backbone
15 min
Non-SSCL trunks
20 min
MP feeders
35 min
LP lifelines
60 min
vs current ~600
+65%
Buses / 1000
0.60
Calibration ✓
+9.7%
v3.3.4 — Aspirational (phase-2)
1,113
buses
SSCL backbone
15 min
Non-SSCL trunks
15 min
MP feeders
30 min
LP lifelines
60 min
vs current ~600
+85%
Buses / 1000
0.67
Calibration ✓
+9.7%
Same engine, same data, same QC. Only the non-SSCL headway target differs. Year-1 commit → v3.3.5. Year-3 ambition → v3.3.4.
Slide 10 · Decision the IAS makes

## Slide 11
What's in Phase 1 vs what comes next (Phase 2)
Concept
Phase 1 (now)
Phase 2 (target)
Walk catchment
400 m Euclidean buffer
OSMnx isochrone clipped against Dal/Anchar/Jhelum
Population
WorldPop 2024 raster
Census 2021 ward + growth-adjusted corridors
Cycle time
Virtual 500m stops + congestion×
Field-timed stop dwell + GPS journey traces
Demand
Static buffer × mode × trips
Demand elasticity (Mohring) + AFC validation
Tourist surge
Tier-3 POI weights + ×1.3
Real arrival data from JKTDC / hotels
Convoy / NH-44
Not modelled
Time-of-day operability mask
Slide 11 · Phase-1 → Phase-2 backlog

## Slide 12
Data we'd need from your office to sharpen v3.4
Phase-2 features above are limited by data, not by maths. Here is the concrete ask.
Priority
Dataset
Custodian
Why it matters
P0
Master stops register
Kashmir_Stops_Sectored_V2.csv
RTOs / SSCL
Retires the 23 TMP-K placeholder route codes.
P0
Operator permit registry (live)
Permit no. · owner · vehicle no. · depot
RTO offices · J&K Transport Commr
Exact displaced vehicles → defensible buyback.
P0
GPS traces — current operators
30 days · 1 Hz · SSCL + private operators
SSCL CHALO ops · MTS Kashmir
Replaces OSRM free-flow + congestion×2.2 model.
P1
Census 2021 ward-level population
Ward boundaries + counts
Census of India · J&K Directorate
Tighter Pop_Score → tighter CDI bands.
P1
AFC / fare-card ridership (per route)
Per-route per-day boardings
SSCL CHALO platform
Enables route-level demand & Mohring elasticity.
P1
JKTDC tourist arrival data
Daily arrivals · Gulmarg / Pahalgam / Sonamarg
J&K Tourism Dept (JKTDC)
Real seasonal surge → tourist fleet sizing.
P2
Road operability calendar
NH-44 convoys · Sinthan / Z-Morh / Mughal Road dates
BRO · J&K Traffic · Border Mgmt
Auto-flag Winter_Suspended; subtract un-operable hours.
P2
Bus stop / depot inventory
Lat-lon of every stop · depot capacity
SSCL / JKRTC / RTO offices
Replaces virtual 500 m stop spacing.
P2
Bridge load / road-width registry
Per-bridge weight limit · arterial road widths
R&B Dept · MC Srinagar
Restricts 12 m HPV to roads/bridges that can take it.
Priority key:
P0
blocks v3.4 calibration
P1
improves accuracy meaningfully
P2
future-state polish
Slide 12 · Data we need from your office

## Slide 13
What this output is — and what it is not
WHAT IT IS
✓
207 active routes classified with HP / MP / LP bands
✓
Fleet sized for phase-1 conservative headways (15/20/35/60 min)
✓
30 SSCL backbone routes calibrated against CHALO Apr 2026 data
✓
9-sheet RTO workbook with operator absorption + buyback estimates
✓
Reproducible pipeline — every number traces to a CSV row
WHAT IT IS NOT
✗
A ridership survey — field validation still required
✗
A net-fleet-gap report — current ops verification needed
✗
Final headway commitments — RTO consultation still pending
✗
A buyback price commitment — figures are estimates per peer cities
✗
Tourist demand model — surge data is Phase 2 work
Slide 13 · Honest scope

## Slide 14
Recommended Path
Five asks for the IAS
1
Sign-off
Approve v3.3.5 conservative phase-1 plan at the Stage-1 review.
2
Operator dialogue
Authorise consultation with All J&K Transport Welfare Association.
3
Phased rollout
Activate SSCL backbone + 20-min trunks first; expand on observed ridership.
4
Monthly recalib
Re-run cross_evaluate vs CHALO monthly; recalibrate CAPTURE_SCALE if drift > ±15%.
5
Phase-2 scope
Sanction next-FY work — OSMnx walksheds, demand elasticity, convoy mask.
Engine v3.3.5 · Companion artefacts: RTO 9-sheet workbook · Headway PDF study guide · Live dashboard at bus-sathi-dashboard