## Slide 1
KASHMIR VALLEY PUBLIC TRANSPORT
Route Rationalisation Plan
A data-driven service plan for the Srinagar Valley bus network, built on the Srinagar Smart City electric-bus backbone.
ACTIVE ROUTES
207
clear, non-overlapping lines
TOTAL BUSES
1,009
recommended for the network
LONGEST WAIT
35 min
anywhere on the network
RESIDENTS
70%
covered within a short walk
Prepared for the Principal Secretary (Transport), Government of Jammu & Kashmir · for planning review ahead of operator consultation.

## Slide 2
Why this plan exists
Srinagar's bus network grew permit by permit, with no central frequency plan.
Wasteful duplication
More than a dozen buses chase the same riders on the Parimpora–Lal Chowk–Dalgate corridor, while whole neighbourhoods get nothing.
Transit deserts
The southern industrial belt (Khonmoh, Rangreth) and satellite towns (Ganderbal, Pulwama) are badly under-served.
No reliability
Without a published frequency, buses bunch together at peak hours and disappear off-peak — riders cannot plan around them.
Wrong bus, wrong road
Large buses are sent down narrow old-city lanes, while small minibuses run long inter-district highways.
Built around half the riders
Almost two-thirds of riders are women, yet the network was never designed around where they actually travel.
Slide 2 · The problem

## Slide 3
How the plan is built — four stages
STAGE 1
Gather
Every registered route permit in the valley
Real road driving times on the live map
Where people live, from a satellite population grid
The places people travel to (hospitals, colleges, markets)
STAGE 2
Measure demand
Population living within a short walk of each route
The destinations each route reaches, weighted by importance
Extra weight for women's destinations and tourist corridors
STAGE 3
Rank and size
Rank every route by how much travel it serves
Group routes into high, medium and low priority
Choose how often buses run on each
Work out how many buses that needs
STAGE 4
Check and publish
Eight automatic quality checks before anything is released
Compare against real electric-bus ridership as a sanity check
Publish the route plan, maps and the operator workbook
Slide 3 · Method, stage by stage

## Slide 4
From 342 permits to 207 clear routes
Duplicate permits are merged into unified trunk lines; the rest are kept as feeders.
50
157
135
Upgraded to trunk line
50 routes · 15% of permits
Kept as feeder
157 routes · 46% of permits
Merged into a trunk
135 routes · 39% of permits
What changes for the rider
The 207 active routes are a clear, legible network instead of 342 overlapping permits. Trunk lines carry the busiest corridors at high frequency; feeders connect neighbourhoods into them; and the merged 135 permits stop competing for the same passengers.
Slide 4 · Network composition

## Slide 5
Recommended fleet — 1,009 buses
80 large (12-metre) + 807 medium (9-metre) + 122 small (minibus)
Large bus
80
12-metre standard low-floor
about 50 seats · 8% of the fleet
Medium bus
807
9-metre electric / midi bus
about 35 seats · 80% of the fleet
Small bus
122
minibus / tempo traveller
about 15 seats · 12% of the fleet
On trunk corridors the large and medium buses are kept to a balanced fifty-fifty mix, so neither size dominates a route.
Slide 5 · Fleet composition

## Slide 6
The electric-bus backbone
The plan is anchored on the existing Srinagar Smart City electric-bus routes.
30
Official Smart City electric-bus routes
already operating
45
Matching permits in the dataset
duplicate operators
8.0
Buses per route recommended
at a 15-minute service
+9.7%
Above the frequency-matched fleet benchmark
comfortably within tolerance
Operators absorbed into the new network — indicative compensation
Operator type
Permits
Recommended action
Indicative cost
Private minibus
100
Buy back at about Rs 15 lakh each
Rs 15.00 Cr
Small bus / tempo
34
Reassign to last-mile feeder duty
Rs 1.02 Cr
Large bus
1
Absorb into the public fleet
Rs 0.50 Cr
Total absorbed
135
Mixed strategy, by consultation
Rs 16.52 Cr
Costs are indicative estimates from peer-city averages — not a price commitment.
Slide 6 · Backbone and operator absorption

## Slide 7
How often buses run
Buses are spaced by wait time. No route in the plan waits longer than 35 minutes.
0 min
10 min
20 min
30 min
40 min
Smart City electric backbone
every 15 min
45 routes · the busiest corridors
Main trunk lines
every 20 min
85 routes · high-demand routes
Feeders and lifeline routes
every 35 min
77 routes · neighbourhood & rural links
Earlier drafts allowed one-hour waits on lifeline routes; those have been removed — the longest wait anywhere is now 35 minutes.
Slide 7 · Service frequency

## Slide 8
The methodology, stated in full
Every number rests on a standard transit-planning formula. Here they are, written out.
Number of buses on a route = round-trip time divided by how often a bus runs, rounded up, plus a 15% spare allowance for maintenance and breakdowns.
Buses = round-trip time ÷ wait between buses (rounded up) × 1.15
Basis: Vuchic (2005); Ceder (2007); spare allowance per industry practice.
Round-trip time = driving time both ways + time spent at stops + junction delays + peak-hour congestion + a recovery buffer to keep to schedule.
round-trip time = driving + stops + junctions + congestion + recovery
Basis: Transit Capacity & Quality of Service Manual (Transportation Research Board, 2013).
Estimated daily riders = people within a short walk × the share who take the bus × trips per day × the route's share of a shared corridor × a calibration factor. It is computed automatically from open data, with no operator GPS feed needed.
riders = walk-up population × bus share × trips × corridor share × factor
Basis: Gravity / accessibility model — Hansen (1959); Ortúzar & Willumsen (2011).
Composite Demand Index = half the population score + half the destinations score. Routes are then grouped into high, medium and low priority, which sets how often buses run on each.
demand index = ½ population + ½ destinations → natural-breaks grouping
Basis: Natural-breaks classification — Jenks (1967).
Slide 8 · Formulas and their basis

## Slide 9
Sources and references
The data behind the plan, and the published research behind each method.
Population
WorldPop satellite-derived population grid (Tatem, 2017); Census of India 2011; Srinagar Smart City detailed project report.
Road network & travel time
OpenStreetMap road data; routing by the open-source routing engine OSRM (Luxen & Vetter, 2011).
Destinations
Points of interest from OpenStreetMap (hospitals, colleges, markets, offices).
Walking distance
Four-hundred-metre walk catchment, about a five-minute walk (El-Geneidy et al., 2014).
Buses & frequency
Vuchic, Urban Transit (2005); Ceder, Public Transit Planning and Operation (2007).
Cycle & recovery time
Transit Capacity and Quality of Service Manual, Transportation Research Board (2013).
Demand
Hansen, accessibility model (1959); Ortúzar & Willumsen, Modelling Transport (2011).
Ridership check
Srinagar Smart City electric-bus published ridership totals (an aggregate figure — no individual GPS or fare-card traces are used).
Slide 9 · Sources and references

## Slide 10
How the fleet compares with other Indian cities
Buses per one thousand residents — the plan sits comfortably in the peer-city range.
Mysuru
0.35
Bhopal
0.43
Indore
0.45
Bengaluru (BMTC)
0.51
Srinagar (this plan)
0.61
Chandigarh
0.65
Pune
0.75
Delhi
0.90
Mumbai
1.20
At 0.61 buses per thousand residents, Srinagar is closest to Chandigarh — comparable in size, terrain and scope.
Slide 10 · Peer-city comparison

## Slide 11
What is modelled today, and how it sharpens with more data
The method is sound today and improves as official datasets become available.
Concept
Modelled today
Sharper with official data
Walking distance
Straight-line walk catchment
Street-network walk paths around lakes and the river
Population
Satellite population grid
Ward-level census counts
Travel time
Open routing-engine estimate with a congestion factor
Measured bus speeds from the field
Demand
Population-based estimate
Fare-card ridership, route by route
Tourist demand
Weighted tourist destinations
Actual visitor-arrival figures
Road closures
Not yet modelled
Highway-convoy and winter-closure calendar
Slide 11 · Today's model and its refinements

## Slide 12
Data we would value from your office
These refinements are limited by data availability, not by method. The concrete ask:
Priority
Dataset
Why it matters
Most useful
Bus position records from current operators
A few weeks of location traces
Replaces the open routing-engine travel-time estimate with measured speeds.
Valuable
Ward-level population from the latest census
Ward boundaries and counts
Sharpens the demand score and the priority grouping.
Valuable
Fare-card ridership, route by route
Daily boardings per route
Enables true route-level demand and frequency-induced ridership.
Valuable
Tourist arrival figures
Daily arrivals for Gulmarg, Pahalgam, Sonamarg
Lets us size the seasonal tourist fleet on real numbers.
Future
Road-operability calendar
Convoy and winter-closure dates
Automatically stands down routes that cannot run in winter.
Future
Bridge-weight and road-width register
Per-bridge limits and arterial widths
Keeps large buses off roads and bridges that cannot take them.
Slide 12 · Data request

## Slide 13
What this plan is — and what it is not
WHAT IT IS
✓
207 active routes, ranked by demand and grouped into priority tiers
✓
Buses sized for a published frequency — every 15, 20 or 35 minutes
✓
Anchored on the Smart City electric-bus routes, checked against their ridership
✓
An operator workbook with absorption and indicative compensation
✓
A fully reproducible analysis — every number traces back to its source
WHAT IT IS NOT
✗
A passenger survey — on-the-ground validation is still advisable
✗
A statement of the exact extra buses needed versus those running today
✗
Final, committed frequencies — these follow operator consultation
✗
A compensation price — the figures are indicative estimates
✗
A tourist-demand model — that needs real arrival data
Slide 13 · Honest scope