## Slide 1
TECHNICAL BRIEFING
Kashmir Valley Transit Engine
Technical Briefing — v3.3.7 Open-data pipeline, methodology, formulas and literature backing, for the engineering and data-review audience.
Engine v3.3.7 • May 2026 • Phase-1 plan • 35-min headway ceiling • balanced 50/50 trunk fleet • fully open-data & reproducible

## Slide 2
Scope & open-data inputs
100% open / reproducible
342
permits in scope
33.5–34.5°N
Srinagar Valley bbox
1.66M
study-area residents
4
open data sources
Population — WorldPop 100 m raster (cropped to study area); Census 2011 + Smart-City DPR baseline.
Points of interest — OpenStreetMap via the Overpass API, classified into a 3-tier vocabulary.
Road network & travel time — OSRM (local Docker, Kashmir OSM extract) with a circuity fallback.
SSCL e-bus backbone — 30 published Srinagar Smart City routes injected as synthetic trunks.
No proprietary GPS / AFC feed is required — the whole pipeline runs on open data and is re-runnable.
Slide 2 • Inputs are open data — anyone can reproduce the run

## Slide 3
Pipeline architecture — four phases
1 · Ingestion
• Column-alias loader
• OSRM geometry
• Bbox clip
• SSCL backbone inject
2 · Spatial
• 400 m walk catchments
• WorldPop zonal stats
• POI gravity (250 m)
• Overlap clustering
3 · Classify
• CDI = ½Pop + ½POI
• Jenks → HP/MP/LP
• Social-obligation floor
• SSCL → trunk/HP
4 · Fleet + export
• Cycle time → headway
• Fleet = ⌈C/h⌉ × 1.15
• HPV/MPV 50/50 split
• CSV · maps · workbook
Demand KPIs are derived after fleet locks (no feedback loop) — classification stays demand-driven, not fleet-driven.
Slide 3 • Deterministic 4-phase pipeline

## Slide 4
Network result at a glance
207
active routes (T50/F157)
1,009
total buses
35 min
max wait, anywhere
69.8%
population covered
Chart: Fleet mix (balanced 50/50 on trunks)
| HPV 12 m | MPV 9 m | LPV mini
Fleet | 80 | 807 | 122
Chart: Headways present (only 15 / 20 / 35)
| 15 min | 20 min | 35 min
Routes | 45 | 85 | 77
Slide 4 • Live from Rationalised_Routes_Kashmir_v3.csv

## Slide 5
Methodology — cycle time
Cycle = 2 × OSRM running time + stop dwell + junction/turn penalty + congestion × + bridge queue + recovery
Why: round-trip running time plus a recovery/layover allowance absorbs traffic variability and keeps the schedule honest; the ×2.2 downtown congestion multiplier and +8 min Jhelum-bridge queue reflect observed peak conditions.
Source: TCQSM (TRB 2013); Vuchic (2005).
Running time comes from OSRM on the real road graph — not straight-line distance.
Dwell = estimated stops × 0.5 min (≈30 s/stop); junction & sharp-turn penalties added per geometry.
A per-km sanity cap clips OSRM glitches on long inter-district highways.
Recovery time is what lets a published headway actually hold in service.
Slide 5 • compute_cycle_times()

## Slide 6
Methodology — headway & fleet
Fleet N = ⌈ Cycle time ÷ Headway ⌉ × spare ratio (1.15)
Why: to run a bus every h minutes on a route whose round trip takes C minutes you need ⌈C/h⌉ vehicles; the 15% spare ratio covers maintenance, breakdown rotation and depot reserve.
Source: Vuchic (2005); Ceder (2007); spare ratio per APTA practice.
Headway h ≤ 35 min (ceiling) · SSCL backbone 15 min · HP trunks 20 min
Why: a hard service-quality ceiling guarantees no rider waits more than 35 minutes; trunk targets follow demand and SSCL's own published design frequency.
Source: TCQSM Quality-of-Service framework (TRB 2013).
Trunk vehicle split is balanced 50/50 HPV/MPV — neither class dominates a corridor (RTO ask).
SSCL empirical fleet is treated as a floor, not a cap: the formula can raise it where the cycle demands.
Slide 6 • step8/step9 fleet & vehicle split

## Slide 7
Methodology — automatic demand model
Daily demand = Walkshed pop × mode share × trip rate × corridor share × capture scale (0.18)
Why: a gravity/accessibility estimate from open data — population within a 400 m walk, scaled by realistic mode share and trip rate, then apportioned across competing routes by relative frequency.
Source: Hansen (1959); Ortúzar & Willumsen (2011); 400 m per El-Geneidy et al. (2014).
Fully automatic and open-data driven — it needs no live GPS or AFC feed from any operator app.
The 0.18 capture scalar was calibrated ONCE against SSCL/CHALO published annual ridership totals (an aggregate public figure — not GPS traces), and is a fixed constant thereafter.
Sanity check: engine SSCL daily demand 34,545 vs published ≈ 31,869 (+8%, within band).
Fleet sizing is independent of this demand figure — supply is sized to the target service level.
Slide 7 • compute_phase4_metrics() — open-data demand

## Slide 8
Methodology — classification (CDI + Jenks)
Final CDI = 0.50 × Population score + 0.50 × POI gravity score
Why: a composite demand index blends who lives near the route with what destinations it reaches; Road_Multiplier is only a tie-breaker near a band edge, never a multiplier on CDI.
Source: Gravity model: Hansen (1959). Banding: Jenks natural breaks (1967).
Jenks natural breaks split the CDI distribution into High / Medium / Low priority bands.
SSCL backbone routes bypass classification — forced to trunk / HP at a 15-min target.
Social-obligation routes (87 flagged) get an LP→MP floor: hospitals, KP townships, women's colleges.
Slide 8 • step4a/step5 classification

## Slide 9
Calibration & quality control
Check | Result | Target
Per-route SSCL fleet vs headway-scaled published CHALO | +9.7% | within ±25%
SSCL daily demand vs published aggregate | +8% | within ±15%
Automated QC checks (block export on fail) | 8/8 passing | 8/8
Red_Overload routes | 0 | 0
Route codes assigned | 342 / 342 | all coded
Calibration uses CHALO's PUBLISHED ridership totals only — the model itself needs no live feed.
Slide 9 • run_all_qc_checks() + cross_evaluate.py

## Slide 10
Known limitations (v4 backlog)
1. Euclidean walksheds over-count near Dal/Anchar/Hokersar lakes & the Jhelum (walking barriers).
2. Binary winter toggle — full 4-season stratification not yet modelled.
3. Tourist surge captured via Tier-3 POI weights, not actual arrival counts.
4. Military / convoy operability windows on NH-44 not yet subtracted.
5. No demand elasticity (Mohring) — Load_Ratio assumes today's ridership at improved frequency.
6. Per-route AFC validation still manual; calibration is system-level.
Slide 10 • Honest limitations

## Slide 11
Sources & methodology references
Every formula and parameter in this plan is grounded in the standard transit-planning literature:
Fleet sizing N = ⌈C / h⌉
Vuchic, V. R. (2005) Urban Transit: Operations, Planning & Economics, Wiley; Ceder, A. (2007) Public Transit Planning and Operation, Elsevier.
Cycle time, dwell & recovery
TRB (2013) Transit Capacity & Quality of Service Manual, 3rd ed. (TCRP Report 165).
Spare ratio (10–20%)
APTA standard operating practice; TCQSM recovery/layover guidance.
Frequency / headway LOS
TCQSM (2013) Ch.5 Quality of Service; Ceder (2007) frequency-setting methods.
Demand — gravity / accessibility
Hansen, W. (1959) How Accessibility Shapes Land Use, JAPA 25(2); Ortúzar & Willumsen (2011) Modelling Transport, 4th ed., Wiley.
400 m walk catchment (~5 min)
El-Geneidy et al. (2014) New evidence on walking distances to transit, Transportation 41.
Natural-breaks classification
Jenks, G. (1967) The Data Model Concept in Statistical Mapping, Int. Yearbook of Cartography.
Population raster
Tatem, A. (2017) WorldPop, open data for spatial demography, Scientific Data 4:170004; Census of India 2011 + Srinagar Smart City DPR.
Road network & routing
Luxen & Vetter (2011) Real-time routing with OpenStreetMap data, ACM SIGSPATIAL (OSRM).
Points of interest
OpenStreetMap contributors (2024), via the Overpass API.
Ridership calibration anchor
SSCL / CHALO Srinagar e-bus published ridership, May 2025–Apr 2026 (aggregate totals only — no GPS/AFC traces used).
References • transit-planning literature backing each design choice

## Slide 12
Reproducible & versioned
Deliverables (outputs_v3.3.7/):
• Kashmir_Route_Frequency_Plan_v3.3.7_RTO.xlsx (9-sheet) + _RTO_Pretty.xlsx (bus schedule)
• Master_Transit_Map_Kashmir_v3.html + 192 per-route maps
• Rationalised_Routes_Kashmir_v3.csv / .geojson · Rationalisation_Log · Passenger_Impact
Every number traces back to a CSV row and an open-data source.
Source: github.com/Princu-Babu/kashmir-transit-rationalisation
Slide 12 • Deliverables