## Slide 1
GOVERNMENT BRIEFING
Srinagar Bus Network Rationalisation
Briefing for the Principal Secretary (Transport), RTO leadership and IAS reviewers. A data-driven plan to make Srinagar's buses reliable, equitable and operator-fair.
Engine v3.3.8 • June 2026 • Phase-1 plan • 35-min headway ceiling • balanced 50/50 trunk fleet • fully open-data & reproducible

## Slide 2
Why this plan exists
Srinagar's bus network grew organically over decades — 613 permits, no central frequency plan:
• Heavy duplication on Parimpora–Pantha Chowk–Dalgate (15+ buses chasing the same riders).
• Transit deserts in the south industrial belt (Khonmoh, Rangreth) and satellite towns.
• No headway discipline — buses bunch at peak and vanish off-peak.
• Wrong vehicle on the wrong road — big buses in narrow lanes, minibuses on 40-km highways.
• 64.5% of riders are women, yet the network was never designed around that.
Slide 2 • The problem

## Slide 3
The plan, in numbers
172
clear routes
1,053
buses (Phase-1)
+76%
over today's ~600
35 min
longest wait anywhere
43
trunk routes
129
feeder routes
448
duplicates absorbed
38%
residents covered
One confirmed plan — Phase-1 — about 1,053 buses, deployable in Year-1. Fleet density 0.55 buses / 1,000 residents (peer-city band).
Slide 3 • Phase-1 is the plan

## Slide 4
How the plan was built
Look
• Every route + where people live
• & which places they need
Score
• Rank each route by real demand
• (population + destinations)
Tidy up
• Merge duplicate permits
• into clear trunk lines
Set service
• Buses every 15–35 min
• right bus for each road
Built entirely on open data (population, maps, road network) — no proprietary feed needed, so it is transparent and re-runnable.
Slide 4 • Method in plain language

## Slide 5
Fleet & how often buses run
Chart: Recommended fleet mix
| Large (12 m) | Medium (9 m) | Mini
Fleet | 170 | 799 | 84
Chart: How often a bus comes
| every 15 min | every 20 min | every 35 min
Routes | 41 | 22 | 109
No route in the plan waits longer than 35 minutes — the 1-hour waits are gone.
Slide 5 • Frequency & fleet

## Slide 6
Why you can trust the numbers
Standard methods, not guesswork — every formula follows the transit-planning literature:
• Fleet = round-trip time ÷ headway, + 15% spare — Vuchic (2005), Ceder (2007), APTA practice.
• Cycle & recovery time — Transit Capacity & Quality of Service Manual (TRB, 2013).
• Demand from population + destinations (gravity model) — Hansen (1959); Ortúzar & Willumsen (2011).
• Real road travel times (OSRM) and real population (WorldPop, Census 2011).
• Calibrated against SSCL/CHALO published ridership — engine is within ±25% on per-route fleet, 8/8 QC checks pass.
Full source list on the references slide — the plan is auditable end to end.
Slide 6 • Credibility & sources

## Slide 7
Equity, women & social obligation
64.5%
riders are women
+25%
weight on women-anchor POIs
211
social-obligation routes
7
tourist corridors flagged
Women-anchor destinations (women's colleges, maternity hospitals, women's markets) get a +25% demand weight.
Social-obligation routes are protected with a service floor regardless of raw demand: KP townships
(Sheikhpora, Vessu, Mattan), major hospitals (SKIMS, SMHS, LD), and inter-district lifelines.
Tourist & seasonal flags mean snow-affected corridors run reduced winter service rather than being dropped.
Slide 7 • Nobody left behind

## Slide 8
Operator impact (carefully accounted)
Operator class | Permits absorbed | Recommended action
Private minibus | 329 | Buyback / reassign to feeder service
LPV / tempo | 75 | Reassign to last-mile / feeder duty
HPV bus | 1 | Roll into JKRTC / SSCL e-bus
JKRTC / city bus | 34 | Retain on MP / LP routes
Total | 448 | Operator-welfare consultation before rollout
Each absorbed permit is logged with its reasoning in Rationalisation_Log_Kashmir_v3.csv.
Engagement with the All J&K Transport Welfare Association is recommended before any route change.
Slide 8 • Fair to operators

## Slide 9
Implementation roadmap
Weeks 0–2
• Government sign-off
• Circulate workbook + map
Weeks 2–6
• Operator consultation
• Finalise buyback policy
Months 2–6
• Phased rollout
• Trunks first, then feeders
Ongoing
• Monitor & recalibrate
• Annual data refresh
Slide 9 • Rollout

## Slide 10
What we ask of you
1. Sign off the Phase-1 rationalised network (≈ 1,053 buses) at the Stage-1 review.
2. Authorise operator consultation with the All J&K Transport Welfare Association.
3. Approve a phased rollout starting with the SSCL backbone + trunk corridors.
4. Confirm an annual data refresh & recalibration cycle.
5. Sanction v4 scoping (network-graph walksheds, demand elasticity) for next FY.
Slide 10 • Asks

## Slide 11
Sources & methodology references
Every formula and parameter in this plan is grounded in the standard transit-planning literature:
Fleet sizing N = ⌈C / h⌉
Vuchic, V. R. (2005) Urban Transit: Operations, Planning & Economics, Wiley; Ceder, A. (2007) Public Transit Planning and Operation, Elsevier.
Cycle time, dwell & recovery
TRB (2013) Transit Capacity & Quality of Service Manual, 3rd ed. (TCRP Report 165).
Spare ratio (10–20%)
APTA standard operating practice; TCQSM recovery/layover guidance.
Frequency / headway LOS
TCQSM (2013) Ch.5 Quality of Service; Ceder (2007) frequency-setting methods.
Demand — gravity / accessibility
Hansen, W. (1959) How Accessibility Shapes Land Use, JAPA 25(2); Ortúzar & Willumsen (2011) Modelling Transport, 4th ed., Wiley.
400 m walk catchment (~5 min)
El-Geneidy et al. (2014) New evidence on walking distances to transit, Transportation 41.
Natural-breaks classification
Jenks, G. (1967) The Data Model Concept in Statistical Mapping, Int. Yearbook of Cartography.
Population raster
Tatem, A. (2017) WorldPop, open data for spatial demography, Scientific Data 4:170004; Census of India 2011 + Srinagar Smart City DPR.
Road network & routing
Luxen & Vetter (2011) Real-time routing with OpenStreetMap data, ACM SIGSPATIAL (OSRM).
Points of interest
OpenStreetMap contributors (2024), via the Overpass API.
Ridership calibration anchor
SSCL / CHALO Srinagar e-bus published ridership, May 2025–Apr 2026 (aggregate totals only — no GPS/AFC traces used).
References • transit-planning literature backing each design choice

## Slide 12
Thank you
This plan is reproducible, auditable and re-runnable.
Every number traces back to open data and a published source.
The bus-schedule workbook and interactive map are on the dashboard for one-click access.
Source & audit log: github.com/Princu-Babu/kashmir-transit-rationalisation
Slide 12 • Close